## Slide 1: Embedded Computer Systems

## Slide 2: Digital System v. Embedded System
Digital System: may provide service
  as a self-contained unit (e.g., desktop PC)
  as part of a larger system (e.g., digital control system for manufacturing plant)
Embedded System:
  part of a larger unit
  provides dedicated service to that unit
G. De Micheli and R. Gupta, “Hardware/Software Co-Design,” Proceedings of the IEEE, 85(3), March 1997, pp. 349-365

## Slide 3: Embedded Systems Overview
Computing systems are everywhere
Most of us think of “desktop” computers
  PC’s
  Laptops
  Mainframes
  Servers
But there’s another type of computing system
  Far more common...
F. Vahid and T. Givargis, Embedded System Design: A Unified Hardware/Software Introduction, John Wiley & Sons, 2002.

## Slide 4: Embedded Systems Overview (cont.)
Embedded computing systems
  Computing systems embedded within electronic devices
  Hard to define. Nearly any computing system other than a desktop computer
  Billions of units produced yearly, versus millions of desktop units
  Perhaps 100s per household and per automobile
Computers are in here...
and here...
and even here...
Lots more of these, though they cost a lot less each.

## Slide 6: A “Short List” of Embedded Systems
And the list goes on and on
Anti-lock brakes
Auto-focus cameras
Automatic teller machines
Automatic toll systems
Automatic transmission
Avionic systems
Battery chargers
Camcorders
Cell phones
Cell-phone base stations
Cordless phones
Cruise control
Curbside check-in systems
Digital cameras
Disk drives
Electronic card readers
Electronic instruments
Electronic toys/games
Factory control
Fax machines
Fingerprint identifiers
Home security systems
Life-support systems
Medical testing systems
Modems
MPEG decoders
Network cards
Network switches/routers
On-board navigation
Pagers
Photocopiers
Point-of-sale systems
Portable video games
Printers
Satellite phones
Scanners
Smart ovens/dishwashers
Speech recognizers
Stereo systems
Teleconferencing systems
Televisions
Temperature controllers
Theft tracking systems
TV set-top boxes
VCR’s, DVD players
Video game consoles
Video phones
Washers and dryers

## Slide 7: Examples of Embedded Systems
PC having dedicated software programs and appropriate interfaces to a manufacturing assembly line
Microprocessor dedicated to a control function in a computer, e.g., keyboard/mouse input control

## Slide 8: Outline
Embedded systems overview
Design challenge – optimizing design metrics
Technologies
  Processor technologies
  Design technologies
Generic codesign methodology

## Slide 9: Some Application Domains
CONSUMER PRODUCTS
  Appliances, Games, A/V, Intelligent home devices
TRANSPORTATION
  Autos, Trains, Ships, Aircrafts
PLANT CONTROL
  Manufacturing, Chemical, Power Generation
NETWORKS
  Telecommunication, Defense
Local
  e.g., appliance
Locally distributed
  e.g., aircraft control over a LAN
Geographically distributed
  e.g., telephone network

## Slide 10: Parts of an Embedded System
HARDWIRED UNIT
Application-specific logic
Timers
A/D and D/A conversion
MEMORY
PROCESSOR
SENSORS
ACTUATORS
EMBEDDED SYSTEM
ENVIRONMENT
USER
I/O

## Slide 11: Parts of an Embedded System (cont.)
Actuators - mechanical components (e.g., valve)
Sensors - input data (e.g., accelerometer for airbag control)
Data conversion, storage, processing
Decision-making
Range of implementation options
Single-chip implementation: system on a chip

## Slide 12: Functions and Design Criteria
Monitoring and control functions for the overall system (e.g., vehicle control)
Information-processing functions (e.g., telecommunication system -- data compression, routing, etc.)
Criteria: performance, reliability, availability, safety, usability, etc.

## Slide 13: Some Common Characteristics
Single-functioned
  Executes a single program, repeatedly
Tightly-constrained
  Low cost, low power, small, fast, etc.
Reactive and real-time
  Continually reacts to changes in the system’s environment
  Must compute certain results in real-time without delay

## Slide 14: An Embedded System Example
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Single-functioned -- always a digital camera
Tightly-constrained -- Low cost, low power, small, fast
Reactive and real-time -- only to a small extent
Digital Camera

## Slide 15: Design Challenge – Optimization
Obvious design goal:
  Construct an implementation with desired functionality
Key design challenge:
  Simultaneously optimize numerous design metrics
Design metric
  A measurable feature of a system’s implementation
  Optimizing design metrics is a key challenge

## Slide 16: Design Challenge – Optimization (cont.)
Common metrics
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): The one-time monetary cost of designing the system
  Size: the physical space required by the system
  Performance: the execution time or throughput of the system
  Power: the amount of power consumed by the system
  Flexibility: the ability to change the functionality of the system without incurring heavy NRE cost

## Slide 17: Design Challenge – Optimization (cont.)
Common metrics (continued)
  Time-to-prototype: the time needed to build a working version of the system
  Time-to-market: the time required to develop a system to the point that it can be released and sold to customers
  Maintainability: the ability to modify the system after its initial release
  Correctness, safety, many more

## Slide 18: Design Metric Competition
Expertise with both software and hardware is needed to optimize design metrics
  Not just a hardware or software expert, as is common
  A designer must be comfortable with various technologies
Size
Performance
Power
NRE cost
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Hardware
Software

## Slide 19: Time-to Market
Time required to develop a product to the point it can be sold to customers
Market window
  Period during which the product would have highest sales
Average time-to-market constraint is about 8 months
Delays can be costly
Revenues ($)
Time (months)

## Slide 20: Delayed Market Entry
Simplified revenue model
  Product life = 2W, peak at W
  Time of market entry defines a triangle, representing market penetration
  Triangle area equals revenue
Loss
  The difference between the on-time and delayed triangle areas
On-time Delayed
entry entry
Peak revenue
Peak revenue from delayed entry
Market rise
Market fall
W
2W
Time
D
On-time
Delayed
Revenues ($)

## Slide 21: NRE and Unit Cost Metrics
Costs:
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): the one-time monetary cost of designing the system
  total cost = NRE cost + unit cost * # of units
  per-product cost = total cost / # of units
  = (NRE cost / # of units) + unit cost
Example
  NRE=$2000, unit=$100
  For 10 units
    total cost = $2000 + 10*$100 = $3000
    per-product cost = $2000/10 + $100 = $300
Amortizing NRE cost over the units results in an additional $200 per unit

## Slide 22: NRE and unit cost metrics
Compare technologies by costs -- best depends on quantity
  Technology A: NRE=$2,000, unit=$100
  Technology B: NRE=$30,000, unit=$30
  Technology C: NRE=$100,000, unit=$2
But, must also consider time-to-market

## Slide 23: The Performance Design Metric
Widely-used measure of system, widely-abused
  Clock frequency, instructions per second – not good measures
  Digital camera example – a user cares about how fast it processes images, not clock speed or instructions per second
Latency (response time)
  Time between task start and end
  e.g., Camera’s A and B process images in 0.25 seconds
Throughput
  Tasks per second, e.g. Camera A processes 4 images per second
  Throughput can be more than latency seems to imply due to concurrency, e.g. Camera B may process 8 images per second (by capturing a new image while previous image is being stored).
Speedup of B over S = B’s performance / A’s performance
  Throughput speedup = 8/4 = 2

## Slide 24: Three Key Technologies
Technology
  A manner of accomplishing a task, especially using technical processes, methods, or knowledge
Three key technologies for embedded systems
  Processor technology (CprE 581, 583, 681)
  IC technology (EE 501, 507, 511)
  Design technology (CprE 588)

## Slide 25: Processor Technology
The architecture of the computation engine used to implement a system’s desired functionality
Processor does not have to be programmable
  “Processor” not equal to general-purpose processor
Application-specific
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control logic and State register
Data
memory
IR
PC
Single-purpose (“hardware”)
Datapath
Controller
Control
logic
State register
Data
memory
index
total
+
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory
General-purpose (“software”)

## Slide 26: Processor Technology (cont.)
Processors vary in their customization for the problem at hand
total = 0
for i = 1 to N loop
total += M[i]
end loop
General-purpose processor
Single-purpose processor
Application-specific processor
Desired functionality

## Slide 27: General-Purpose Processors
Programmable device used in a variety of applications
  Also known as “microprocessor”
Features
  Program memory
  General datapath with large register file and general ALU
User benefits
  Low time-to-market and NRE costs
  High flexibility
“Intel/AMD” the most well-known, but there are hundreds of others
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 28: Application-Specific Processors
Programmable processor optimized for a particular class of applications having common characteristics
  Compromise between general-purpose and single-purpose processors
Features
  Program memory
  Optimized datapath
  Special functional units
Benefits
  Some flexibility, good performance, size and power
IR
PC
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 29: Independence of Processor Technologies
Basic tradeoff
  General vs. custom
  With respect to processor technology or IC technology
  The two technologies are independent
General-purpose
processor
ASIP
Single-
purpose
processor
Semi-custom
PLD
Full-custom
General,
providing improved:
Customized,
providing improved:
Power efficiency
Performance
Size
Cost (high volume)
Flexibility
Maintainability
NRE cost
Time- to-prototype
Time-to-market
Cost (low volume)

## Slide 30: Design Technology
The manner in which we convert our concept of desired system functionality into an implementation
Libraries/IP: Incorporates pre-designed implementation from lower abstraction level into higher level.
System
specification
Behavioral
specification
RT
specification
Logic
specification
To final implementation
Compilation/Synthesis: Automates exploration and insertion of implementation details for lower level.
Test/Verification: Ensures correct functionality at each level, thus reducing costly iterations between levels.
Compilation/
Synthesis
Libraries/
IP
Test/
Verification
System
synthesis
Behavior
synthesis
RT
synthesis
Logic
synthesis
Hw/Sw/
OS
Cores
RT
components
Gates/
Cells
Model simulat./
checkers
Hw-Sw
cosimulators
HDL simulators
Gate
simulators

## Slide 31: Design Productivity Exponential Increase
Exponential increase over the past few decades
100,000
10,000
1,000
100
10
1
0.1
0.01
1983
1981
1987
1989
1991
1993
1985
1995
1997
1999
2001
2003
2005
2007
2009
Productivity
(K) Trans./Staff – Mo.

## Slide 32: Design Productivity Gap
While designer productivity has grown at an impressive rate over the past decades, the rate of improvement has not kept pace with chip capacity
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic transistors per chip
(in millions)
100,000
10,000
1000
100
10
1
0.1
0.01
Productivity
(K) Trans./Staff-Mo.
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2003
2005
2007
2009
IC capacity
productivity
Gap

## Slide 33: Design Productivity Gap (cont.)
1981 leading edge chip required 100 designer months
  10,000 transistors / 100 transistors/month
2002 leading edge chip requires 30,000 designer months
  150,000,000 / 5000 transistors/month
Designer cost increase from $1M to $300M
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic transistors per chip
(in millions)
100,000
10,000
1000
100
10
1
0.1
0.01
Productivity
(K) Trans./Staff-Mo.
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2003
2005
2007
2009
IC capacity
productivity
Gap

## Slide 34: The Mythical Man-Month
The situation is even worse than the productivity gap indicates
In theory, adding designers to team reduces project completion time
In reality, productivity per designer decreases due to complexities of team management and communication
In the software community, known as “the mythical man-month” (Brooks 1975)
At some point, can actually lengthen project completion time! (“Too many cooks”)
10
20
30
40
0
10000
20000
30000
40000
50000
60000
43
24
19
16
15
16
18
23
Team
Individual
Months until completion
Number of designers
1M transistors, 1 designer=5000 trans/month
Each additional designer reduces for 100 trans/month
So 2 designers produce 4900 trans/month each

## Slide 35: Co-Design Methodology
Co-design
  Design of systems involving both hardware and software components
  Starts with formal, abstract specification; series of refinements maps to target architecture: allocation, partitioning, scheduling, communication synthesis
  Means to manage large-scale, complex systems
R. Domer, D. Gajski, J. Zhu, “Specification and Design of Embedded Systems,” it+ti magazine, Oldenbourg Verlag (Germany), No. 3, June 1998.

## Slide 36: Complex Systems
SOC (System-On-a-Chip)
  Millions of gates on a chip
    Decreasing processing technologies (deep sub-micron, 0.25 µm and below): decreasing geometry size, increasing chip density
  Problems
    Electronic design automation (EDA) tools
    Time-to-market

## Slide 37: Complex Systems (cont.)
Abstraction
  Reduce the number of objects managed by a design task, e.g., by grouping objects using hierarchy
  Computer-aided design (CAD) example
    Logic level: transistors grouped into gates
    Register transfer level (RTL): gates grouped into registers, ALUs, and other RTL components

## Slide 38: Complex Systems (cont.)
Abstraction
  Co-design example
    System level: processors (off-the-shelf or application-specific), memories, application-specific integrated circuits (ASICs), I/O interfaces, etc.
    Integration of intellectual property (IP) - representations of products of the mind
    Reuse of formerly designed circuits as core cells

## Slide 39: Generic Co-Design Methodology
Synthesis
Specification
Allocation
Partitioning
Scheduling
Communication synthesis
Implementation
Software synthesis
Hardware synthesis
Interface synthesis
model
task
Analysis &
Validation
Note: design models may be captured in the same language

## Slide 40: System Specification
Describes the functionality of the system without specifying the implementation
Describes non-functional properties such as performance, power, cost, and other quality metrics or design constraints
May be executable to allow dynamic verification

## Slide 41: System Specification Example
shared
sync
read
write
sync
B0: top behavior
integer variable
boolean variable
child
behavior
Graphical
representation:
Hierarchy
Concurrency
Transitions between behaviors
Behaviors
Sequential: B1, B2, B3
Concurrent: B4, B5
Atomic: B1
Composite: B2

## Slide 42: System Specification Example (cont.)
shared
sync
read
write
sync
Producer-
consumer
functionality
B6 computes a value
B4 consumes the value
Synchronization is needed: B4 waits until B6 produces the value

## Slide 43: System Specification Example
Atomic behaviors
B1( )
{
stmt;
...
}
B3( )
{
stmt;
...
}
B7( )
{
stmt;
...
}
B6( )
{
int local;
…
shared = local + 1;
signal(sync);
}
B4( )
{
int local;
wait(sync);
local = shared - 1;
...
}

## Slide 44: Allocation
Selects the type and number of components from a library and determines their interconnection
Implements functionality so as to
  Satisfy constraints
  Minimize objective cost function
Result may be customization of a generic target architecture

## Slide 45: Allocation Example
Proc1
LMem1
LMem2
ASIC1
GMem1
IF1
IF2
IF3
system bus
Arbiter1
bus1
bus2
bus3
PE1
PE2
PE: Processing Element
LMem: Local Memory
GMem: Global Memory
IF: Interface
Target Architecture Model

## Slide 46: Partitioning
Defines the mapping between the set of behaviors in the specification and the set of allocated components in the architecture
  Satisfy constraints
  Minimize costs
Not yet near implementation
  Multiple behaviors in a single PE (scheduling)
  Interactions between PEs (communication)
Design model
  additional level of hierarchy
  functional equivalence with specification

## Slide 47: Partitioning Example
System model after partitioning
shared sync B1_start B1_done B4_start B4_done
B1_start
B1_done
B4_start
B4_done
PE0
PE1
Top
B1_ctrl
B4_ctrl
controlling behavior
Child (B1)
assigned to
different PE
than
parent (B0)
synchronization variables

## Slide 48: Partitioning Example (cont.)
Atomic behaviors
B1( )
{
wait(B1_start);
…
signal(B1_done);
}
B3( )
{
stmt;
...
}
B7( )
{
stmt;
...
}
B6( )
{
int local;
…
shared = local + 1;
signal(sync);
}
B4( )
{
int local;
wait(B4_start);
wait(sync);
local = shared - 1;
…
signal(B4_done);
}
B1_ctrl( )
{
signal(B1_start);
wait(B1_done);
}
B4_ctrl( )
{
signal(B4_start);
wait(B4_done);
}

## Slide 49: Scheduling
Given a set of behaviors and optionally a set of performance constraints, determines a total order in time for invoking behaviors running on the same PE
Maintains the partial order imposed by dependencies in the functionality
Minimizes synchronization overhead between PEs and context-switching overhead within each PE

## Slide 50: Scheduling
Ordering information
  Known at compile time
    Static scheduling
    Higher inter-PE synchronization overhead if inaccurate performance estimation, i.e., longer wait times and lower CPU utilization
  Unknown until runtime (e.g., data-, event-dependent)
    Dynamic scheduling
    Higher context-switching overhead (running task blocked, new task scheduled)

## Slide 51: Scheduling Example
shared sync B6_start B3_start
B6_start
sync
B3_start
System model after static scheduling
Scheduling
decision:
Sequential ordering of behaviors on PE0, PE1
Synchronization to maintain partial order across Pes
Optimization - no control behaviors

## Slide 52: Scheduling Example (cont.)
Atomic behaviors
B1( )
{
…
signal(B6_start);
}
B3( )
{
wait(B3_start);
...
}
B7( )
{
stmt;
...
}
B6( )
{
int local;
wait(B6_start);
…
shared = local + 1;
signal(sync);
}
B4( )
{
int local;
wait(sync);
local = shared - 1;
…
signal(B3_start);
}

## Slide 53: Communication Synthesis
Implements the shared-variable accesses between concurrent behaviors using an inter-PE communication scheme
  Shared memory: read or write to a shared-memory address
  Local PE memory: send or receive message-passing calls
Inserts interfaces to communication channels (local or system buses)

## Slide 54: Communication example
lbus0 lbus1 lbus2 sbus
IF0
IF1
IF2
B6
B7
B3
B1
B4
PE0
PE1
Shared_mem
Arbiter
System model after communication synthesis
Synthesis
decision:
Put all global variables into Shared_mem
New global variables in Top

## Slide 55: Communication Example (cont.)
Atomic behaviors
B1( )
{
…
signal (*B6_start_addr);
}
B3( )
{
wait(*B3_start_addr);
...
}
B7( )
{
stmt;
...
}
B6( )
{
int local;
wait (*B6_start_addr);
…
*shared_addr = local + 1;
signal(*sync_addr);
}
B4( )
{
int local;
wait (*sync_addr);
local = *shared_addr - 1;
…
signal (*B3_start_addr);
}

## Slide 56: Communication Example (cont.)
Atomic behaviors
IF0( )
{
stmt;
...
}
Shared_mem( )
{
int shared;
bool sync;
bool B3_start;
bool B6_start;
}
Arbiter( )
{
stmt;
...
}
IF1( )
{
stmt;
...
}
IF2( )
{
stmt;
...
}

## Slide 57: Analysis and Validation
Functional validation of design models at each step using simulation or formal verification
Analysis to estimate quality metrics and make design decisions
Tools
  Static analyzer - program, ASIC metrics
  Simulator - functional, cycle-based, discrete-event
  Debugger - access to state of behaviors
  Profiler - dynamic execution information
  Visualizer - graphical displays of state, data

## Slide 58: Backend
Implementations
  Processor: compiler translates model into machine code
  ASIC: high-level synthesis tool translates model into netlist of RTL components
  Interface
    Special type of ASIC that links a PE with other components
    Implements the behavior of a communication channel

## Slide 59: Summary
Embedded systems are everywhere
Key challenge: optimization of design metrics
  Design metrics compete with one another
A unified view of hardware and software is necessary to improve productivity
Key technologies
  Processor: general-purpose, application-specific, single-purpose
  Design: compilation/synthesis, libraries/IP, test/verification